## Slide 1: Piece-based and flow-based
start of product
end of product
length of product
If length of product is longer than “max. lines in product”, the product will be automatically handled as a flow-based product
Software handles piece- and flow-based product same except for reject timing and statistics.
Unit is ticks (1 tick ~ 0.5 mm)
Use 500-1500 as max.lines in product.

## Slide 2: Timing of reject, piece-based
Reject opens when start of piece is at the reject point, like shown in diagram.
Reject closes when end of piece crosses the reject point + additional time of extra open ticks.
Location of bone within piece does not affect reject timing.
reject
point
bone
reject opens
extra open ticks
reject closes
reject in position “open”
reject in position “closed”

## Slide 3: Timing of reject, flow-based
Reject opens when opening before bone ticks is the distance from the bone to the reject point.
Reject closes when opening after bone ticks is the distance from the bone to the reject point.
reject
point
reject closes
reject opens
reject in position “closed”
reject in position “open”